## Slide 1: T1S Autoconfiguration Tooling
Martin Ruppert
17. Oktober 2024

## Slide 2: Motivation
To give us ESE a learning curve in
  T1S Technology
  C and Pyhton Coding
  Project Working
  git and Github
  MDB Core
  Soft- and Hardware Testing
  Wireshark
This project is not about creating a Software Engineering Company within the Microchip Sales Organization. It is about to learn the processes, structures and vocabulary that our customer are dealing with
All items in the list above could be used in total different customer support processes
And maybe another result could be a proof of concept for customers in the industrial area for an T1S autoconfiguration scenario

## Slide 3: Setup
One Firmware for all 4 boards
Communication between boards should be visible in the OLED1 Extension
Demo should be controllable with only the OLED1 Extension
More complex operations can be done via a terminal
Hardware
  SAME54 Curiosity DM320210
  EVB-LAN8670-RMII EV06P20A
  OLED1 ATOLED1-XPRO
A fifth board is acting as a T1S to 100BaseT Bridge for analyzing the T1S Traffic with Wireshark on a PC
  SAME54 Curiosity DM320210
  LAN8651 MIKROE-5543
  LAN8720A PHY DAUGHTER BOARD AC320004-3

## Slide 4: Github Project
The whole project inclusive all Pyhton Codes and the Presentation is hosted on github at
https://github.com/zabooh/T1S_Autoconf.git
It is a Fork of
https://github.com/Microchip-MPLAB-Harmony/net_10base_t1s.git
from version v1.3.0
The target is to make it official available at https://github.com/MicrochipTech

## Slide 5: MPLABX Project
git clone https://github.com/zabooh/T1S_Autoconf.git

## Slide 6: Set Path to the Harmony Framework Installation

## Slide 7: Content Manager for Framework Repositories
This takes „some“ time

## Slide 8: MCC to re-generate Source Code or modifying

## Slide 9: Programming 4 Boards at the same time
The Tool „multi_progger.pyw“ is a Python Tkinter GUI that controlls 4 instances of the MDB Core simultary.
This allows to keep the connection to four MDB‘s instances and programming four controller at the same time.
If another MPLABX Version should be used than v6.15, this must be changed in the script

## Slide 10: Python GUI for parallel Programming with MDB
More Information about the MDB and how to use it at: https://microchipdeveloper.com/mplabx:mdb
The Pyhton Script starts MDB.bat as a Sub-Process and controlls the input and output. This allows a „remote control“ of the MDB.bat

## Slide 11: MDBCore / background
MPLAX IDE
mdb.bat
mdbcs
mdb.bat
Pre- & postprocess data/memory

## Slide 12: Python GUI for parallel Programming with MDB
„hwtool“ is a MDB command that lists all available debuggers and assigns them an index number. This index number is used to select the debugger
By changing the index number, a debugger can be specifically assigned to a window

## Slide 13: Python GUI for parallel Programming with MDB
With clicking on „Connect MDB“, all setup is done for EDGB, Speed 6Mbit, SWD Interface and selecting the debuggers. This takes some time until it‘s connected
Keep in mind that every mdb.bat process do need about 2 Gbyte of RAM. All four instancess are around 8 Gbyte of RAM

## Slide 14: Python GUI for parallel Programming with MDB
“Prog Boards” programs all Hex files in parallel. The connection to the debugger is maintained so it is not necessary to re-establish the connection again. This allows the programming process to start more quickly.

## Slide 15: Python GUI for testing 4 Boards in parallel
„terminal.pyw“ is the Terminal program that talks with 4 Boards at the same time.
The idea came to me when I was once again completely annoyed by having to arrange TerraTerm four times on my desktop and assigning them to the corresponding COM ports

## Slide 16: Python GUI for testing 4 Boards in parallel
This tool is basically a 4-way Comport Terminal.
There are 4 default COM ports in the upper left, which must be changed to the ones on your machine.
If a COM Port entry is left free, this COM port is not used, so that this tool can be used with less than 4 boards
If you click on “Connect” while all comports are available, then the COM Port Entries go to gray.
If at least one COM Port isn’t available, nothing happens.
If a COM Port entry is left free, this COM port is not used, so that this tool can be used with less than 4 boards
The default ports can be set in the source code

## Slide 17: Python Modules Dependencies „terminal.pyw“
pip install pyserial
https://pythonhosted.org/pyserial/index.html
This module encapsulates the access for the serial port. It provides backends for Python running on Windows, OSX, Linux, BSD (possibly any POSIX compliant system) and IronPython. The module named “serial” automatically selects the appropriate backend.

## Slide 18: Python Modules Dependencies „terminal.pyw“
pip install matplotlib
https://matplotlib.org/
Matplotlib is a comprehensive library for creating static, animated, and interactive visualizations in Python. Matplotlib makes easy things easy and hard things possible.

## Slide 19: Python GUI for testing 4 Boards in parallel
A
B
C
D

## Slide 20: iperf with two boards
A Bandwidth of approx. 9.4 Mbit/sec UDP traffic is achieved between two boards

## Slide 21: 3 iperf client’s at the same time
A Bandwidth of approx. 3.1 Mbits/sec UDP Traffic is achieved when 3 iperf clients are running simultaneously

## Slide 22: Sending the command “netinfo” to all boards
Pre defined commands can be send to one or more boards at the same time when a button is clicked.

## Slide 23: T1S to 100BaseT Bridge

## Slide 24
Bridging
https://github.com/zabooh/t1s_100baset_bridge.git

## Slide 29
-------

## Slide 31: Wireshark

## Slide 32: How to Analyze the Traffic
Managed Switch
1
2
3
4
5
6
7
8
Rest of
the Universe
Personal Computer

## Slide 33: Configuration Software for Managed Switch
Microchip confidential – tentative

## Slide 34: How to Analyze the Traffic
Managed Switch
1
2
3
4
5
6
7
8
Rest of
the Universe
Personal Computer
All traffic on Port 2
is „mirrowed“ to Port 7

## Slide 35
-------

## Slide 36: Software

## Slide 37: OLED1 Display Support
printf for OLED Display

## Slide 39: gfx_mono

## Slide 40: Exception Handler
How to access the Stack Pointer in C

## Slide 41
In case of an Exception this register are put onto the stack automatically:
R0-R3
R12
LR (Link Register)
PC (Program Counter)
PSR (Program Status Register)

## Slide 42
R0-R3 (Registers 0 to 3):
General registers used to store data and intermediate results.
R12 (Register 12):
Also a general register used to store data and intermediate results.
LR (Link Register):
The link register stores the return address of the current program so that normal program flow can be restored after the execution of a subprogram or an exception.
PC (Program Counter):
The program counter is a register that contains the address of the next instruction to be executed in the program code. When an exception occurs, the PC is set to the address of the exception handler.
PSR (Program Status Register):
The Program Status Register contains status information about the status of the processor. This includes flags for the status bits (such as Z, N, C, V), the execution mode (thread or handler mode), the state of the interrupt (enabled or disabled), and other status information.

## Slide 43
Adding a „Bus Fault Exception Test“ command

## Slide 44
readelf –s x.elf
Creates Disassembly Listing File
objdump –S x.elf
Create Symbol List

## Slide 45: Firmware State Machine
And how you can observe that

## Slide 46: Node 0 sends a cyclic Beacon Frame (PLCA Mode)
29,2us
2,128us
27,07us
0
1
2
3
4
5
6
7
In this case it is preconfigured for 8 Nodes. After the Beacon there are 8 Transmit Opportunities (Timeslots)

## Slide 47
Soft-Watchdog-Timeout

## Slide 49: Dump Memory
Like in the good all times

## Slide 51: Heap Managment
How do you find the culprit of a malloc fail?

## Slide 53: Heap Managment
Show Heap Statistics

## Slide 55: Virtual Command Receive
How send Commands by the Firmware